## Slide 1: ASEN 2001 –Lab 1
Computer Analysis of Structures
Session 2

## Slide 2
Input file
You should be at the point at which the input file can be read.
Now it’s time to formulate the equilibrium equations.

## Slide 3
2-D example of formulating the equilibrium equations
10 kN

## Slide 4
Free Body diagram
10 kN
x
y
R2
R1
R3
Notes: Notice point A is a pinned end condition, while point B is a rolling pinned end condition.

## Slide 5
Reaction forces (and reaction moments)
10 kN
R1 = R1uR1
R1 = R1 (uR1,xi + uR1,yj)
R2 = R2uR2
R2 = R2 (uR2,xi + uR2,yj)
R3 = R3uR3
R3 = R3 (uR1,xi + uR1,yj)
x
y
R2
R1
R3
Notes: u represents the unit vectors.

## Slide 6
External forces and moments
10 kN
F1 = F1 (uF1,xi + uF1,yj)
F2 = F2 (uF2,xi + uF2,yj)
F3 = F3 (uF3,xi + uF3,yj)
M1 = M1 (k)
x
y
R2
R1
R3

## Slide 7
Position vectors
10 kN
x
y
rF1 = (rF1,xi + rF1,yj)
rF2 = (rF2,xi + rF2,yj)
rF3 = (rF3,xi + rF3,yj)
rM1 = (rM1,xi + rM1,yj)
rR3 = (rR3,xi + rR3,yj)
rR1 = (rR1,xi + rR1,yj)
rR2 = (rR2,xi + rR2,yj)
R2
R1
R3
Notes: Little r represents the position vectors. Diagonal line rF1 can be represented by its x and y coordinates in the i and j directions.

## Slide 8
10 kN
MF1 = rF1 x F1
M1 = M1 (k)
x
y
R2
R1
R3
MF1 = MF1,z (k)
MF2 = rF2 x F2
MF2 = MF2,z (k)
MF3 = rF3 x F3
MF3 = MF3,z (k)
External moments about A
Notes: Notice here we still have not specified magnitude or direction(polarity) – yet! Still general. Moments on structure due to EXTERNAL sources!!

## Slide 9
10 kN
MR1 = rR1 x R1
x
y
R2
R1
R3
Moments of reactions about A
MR1 = R1 (rR1 x uR1)
MR1 = R1 (rR1 x uR1)k
MR2 = rR2 x R2
MR2 = R2 (rR2 x uR2)
MR2 = R2 (rR2 x uR2)k
MR3 = rR3 x R3
MR3 = R3 (rR3 x uR3)
MR3 = R3 (rR3 x uR3)k
Notes: Now add in the moment contributions from the reaction moments. Again, still general, even though we know moments from R1 and R2 are zero about pt A.

## Slide 10
F1 = F1 (uF1,xi + uF1,yj)
F2 = F2 (uF2,xi + uF2,yj)
F3 = F3 (uF3,xi + uF3,yj)
External Forces
Reaction Forces
R1 = R1 (uR1,xi + uR1,yj)
R2 = R2 (uR2,xi + uR2,yj)
R3 = R3 (uR3,xi + uR3,yj)
External moments
Reaction moments
M1 = M1 (k)
MF1 = MF1,z (k)
MF2 = MF2,z (k)
MF3 = MF3,z (k)
Moments due to external forces
Moments due to external couple moments
MR1 = R1 (rR1 x uR1)k
MR2 = R2 (rR2 x uR2)k
MR3 = R3 (rR3 x uR3)k
Moments due to reaction forces
No reaction couple moments in this example
Equilibrium Equations
+ F1 uF1,x
+ F2 uF2,x
+ F3 uF3,x = 0
R1 uR1,x
+ R2 uR2,x
+ R3 uR3,x
Notes: Bad setup – reactions are on the left now and externals are on the right. Should be switched.

## Slide 11
F1 = F1 (uF1,xi + uF1,yj)
F2 = F2 (uF2,xi + uF2,yj)
F3 = F3 (uF3,xi + uF3,yj)
External Forces
Reaction Forces
R1 = R1 (uR1,xi + uR1,yj)
R2 = R2 (uR2,xi + uR2,yj)
R3 = R3 (uR3,xi + uR3,yj)
External moments
Reaction moments
M1 = M1 (k)
MF1 = MF1,z (k)
MF2 = MF2,z (k)
MF3 = MF3,z (k)
Moments due to external forces
Moments due to external couple moments
MR1 = R1 (rR1 x uR1)k
MR2 = R2 (rR2 x uR2)k
MR3 = R3 (rR3 x uR3)k
Moments due to reaction forces
No reaction couple moments in this example
Equilibrium Equations
+ F1 uF1,x
+ F2 uF2,x
+ F3 uF3,x = 0
R1 uR1,x
+ R2 uR2,x
+ R3 uR3,x
+ F1 uF1,y
+ F2 uF2,y
+ F3 uF3,y = 0
R1 uR1,y
+ R2 uR2,y
+ R3 uR3,y

## Slide 12
F1 = F1 (uF1,xi + uF1,yj)
F2 = F2 (uF2,xi + uF2,yj)
F3 = F3 (uF3,xi + uF3,yj)
External Forces
Reaction Forces
R1 = R1 (uR1,xi + uR1,yj)
R2 = R2 (uR2,xi + uR2,yj)
R3 = R3 (uR3,xi + uR3,yj)
External moments
Reaction moments
M1 = M1 (k)
MF1 = MF1,z (k)
MF2 = MF2,z (k)
MF3 = MF3,z (k)
Moments due to external forces
Moments due to external couple moments
MR1 = R1 (rR1 x uR1)k
MR2 = R2 (rR2 x uR2)k
MR3 = R3 (rR3 x uR3)k
Moments due to reaction forces
No reaction couple moments in this example
Equilibrium Equations
+ F1 uF1,x
+ F2 uF2,x
+ F3 uF3,x = 0
R1 uR1,x
+ R2 uR2,x
+ R3 uR3,x
+ F1 uF1,y
+ F2 uF2,y
+ F3 uF3,y = 0
R1 uR1,y
+ R2 uR2,y
+ R3 uR3,y
+ MF1,z
R1 (rR1 x uR1)
+ R2 (rR2 x uR2)
+ R3 (rR3 x uR3)
+ MF2,z
+ M1 = 0
+ MF3,z

## Slide 13
Equilibrium Equations
+ F1 uF1,x
+ F2 uF2,x
+ F3 uF3,x = 0
R1 uR1,x
+ R2 uR2,x
+ R3 uR3,x
+ F1 uF1,y
+ F2 uF2,y
+ F3 uF3,y = 0
R1 uR1,y
+ R2 uR2,y
+ R3 uR3,y
Known values
= - (F1 uF1,x
+ F2 uF2,x
+ F3 uF3,x)
R1 uR1,x
+ R2 uR2,x
+ R3 uR3,x
= - (F1 uF1,y
+ F2 uF2,y
+ F3 uF3,y)
R1 uR1,y
+ R2 uR2,y
+ R3 uR3,y
= - (MF1,z
R1 (rR1 x uR1)
+ R2 (rR2 x uR2)
+ R3 (rR3 x uR3)
+ MF2,z
+ MF3,z)
In matrix form
+ MF1,z
R1 (rR1 x uR1)
+ R2 (rR2 x uR2)
+ R3 (rR3 x uR3)
+ MF2,z
+ M1 = 0
+ MF3,z
Notes: Known values from external forces and moments. Solve for reactions R1 - R3

## Slide 14
10 kN
x
y
R2
R1
R3
Equilibrium equations for this example in matrix form
Notes: Top row Fx sum, second row Fy sum, last row Mz sum. All external forces cause negative moments: (5x2+10+6x2+8x4) = 64