## Slide 1: Lab 2 – Truss Design
2D truss code

## Slide 2: Schedule
Day 1
  Peer evals
  Method of joints
  Setting up Ax=B
  Truss code demo
  Practice kits
Day 2
  FOS, Monte Carlo
  Please review 2012 Lect. 8
Day 3
  CDR checklist
  CDR signup
  Lab report tips
Day 4
  CDR!
  Tube kit material AFTER CDR
  Build truss during this whole week
Day 5
  Demo and test your Truss!

## Slide 3: Example
FE = 1000 N
1
2
3
4
1
2
3
4
5
1, 2, 3, and 4 are the joints
1
,
2
3
4
5
,
,
, and
are the members
Assume the truss is square and sides are of length L.
x
y

## Slide 4: Method of Joint – FBD for each joint
FE
1
2
3
4
F# = magnitude of force in member #
R3
R2
R = Reaction force at support
R1
F1
F1
F2
F2
F5
F5
F4
F4
F3
F3
-u1
u1
u2
-u2
u3
-u5
u5
-u3
-u4
u4
x
y
u1
= -i
For this system
u2
= -j
u3
= cos 45° i
- sin 45° j
u4
= i
u5
= j
= u3x i + u3y j

## Slide 5: Equilibrium of Joint 1
FE
1
F1
F5
Equilibrium of Joint 2
2
F1
F2
F3
u1
-u5
-u1
u2
u3
… (i)
… (ii)
… (iii)
… (iv)

## Slide 6: Equilibrium of Joint 3
Equilibrium of Joint 4
3
R1
F2
F4
-u2
u4
4
R3
R2
F5
F4
F3
u5
-u3
-u4
… (v)
… (vi)
… (vii)
… (viii)

## Slide 7
No. of equations = 2 x no. of joint … since we have 2 equations at each joint
… (i)
… (ii)
… (iii)
… (iv)
… (v)
… (vi)
… (vii)
… (viii)
No. of members + No. of reactions
No. of unknowns =
2 x 4 = 8
5 + 3 = 8
Solve using matrices

## Slide 8: Assemble the system of linearly independent equations
… (i)
… (ii)
… (iii)
… (iv)
… (v)
… (vi)
… (vii)
… (viii)
F1
F2
F3
F4
F5
R1
R2
R3
External
Sum
-F1
-FE
= 0
Joint 1 x-dirn
Joint 1 y-dirn
Joint 2 x-dirn
Joint 2 y-dirn
Joint 3 x-dirn
Joint 3 y-dirn
Joint 4 x-dirn
Joint 4 y-dirn
-F5
= 0
F1
cos45°F3
= 0
-F2
-sin45°F3
= 0
F4
= 0
F2
R1
= 0
-F4
-cos45°F3
R3
= 0
F5
sin45°F3
R2
= 0

## Slide 9: Assemble the system of linearly independent equations
… (i)
… (ii)
… (iii)
… (iv)
… (v)
… (vi)
… (vii)
… (viii)
F1
F2
F3
F4
F5
R1
R2
R3
External
-F1
= FE
Joint 1 x-dirn
Joint 1 y-dirn
Joint 2 x-dirn
Joint 2 y-dirn
Joint 3 x-dirn
Joint 3 y-dirn
Joint 4 x-dirn
Joint 4 y-dirn
-F5
= 0
F1
cos45°F3
= 0
-F2
-sin45°F3
= 0
F4
= 0
F2
R1
= 0
-F4
-cos45°F3
R3
= 0
F5
sin45°F3
R2
= 0
Can write in matrix form! A x = b

## Slide 10: Assemble the system of linearly independent equations
F1
F2
F3
F4
F5
R1
R2
R3
-1
FE
Joint 1 x-dirn
Joint 1 y-dirn
Joint 2 x-dirn
Joint 2 y-dirn
Joint 3 x-dirn
Joint 3 y-dirn
Joint 4 x-dirn
Joint 4 y-dirn
-1
0
1
cos45°
0
-1
-sin45°
0
1
0
1
1
0
-1
-cos45°
1
0
1
sin45°
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
=
A
x
b
=

## Slide 11: A systematic approach
Things we need to know: (i.e. the things in the input file)
1. Location of the joint
2. Which members are connected to which joint - connectivity
3. Where are the reaction and what are their components
4. Where are the external forces and what are their components
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Location of joints
Connectivity
Joint # | x-component direction | y-component direction
3 | 0 | 1
4 | 0 | 1
4 | 1 | 0
Reactions
External Forces
Joint # | x-component | y-component
1 | -FE = 1000 N | 0

## Slide 12: Dealing with force directions – ‘From’ joints and ‘To’ joints
‘From’ joint
‘To’ joint
(XF,YF)
(XT,YT)
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Member N

## Slide 13: Steps to create A-matrix
Start at joint 1:
Assuming that the input information in the tables have been read and stored
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Connectivity
Members 1 and 5 are connected at joint 1.
Note whether joint is a ‘From’ or ‘To’ joint for each member
Joint 1 is a ‘From’ joint for member 1
Joint 1 is a ‘To’ joint for member 5
Form the unit vector for each member force at the joint
Means we are dealing with the 1st and 2nd rows of the A-matrix
Get the members that are connected to joint 1.
Enter coefficients of unknown member force first.
Note the joint that connects to the other end of each member
Member 1 is connected to joint 2
Member 5 is connected from joint 4

## Slide 14: Steps to create A-matrix
Form the unit vector for each member force at the joint
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
If join is a ‘From’ joint use:
Otherwise it is a ‘To’ joint, so use:
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Joint 1 is a ‘From’ joint for member 1
Thus we can fill in the 1st and 2nd row entries in the A-matrix for the F1 column
u1,1 =
(X2 – X1) i + (Y2 – Y1) j
u1,1 =
(0 – L) i + (L – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u1,1 =
(-1) i + (0) j
i.e. Row 1 - Joint 1 x-direction
Column 1 - force F1 column
Coefficient = -1
i.e. Row 2 - Joint 1 y-direction
Column 1 - force F1 column
Coefficient = 0
joint
Member

## Slide 15: Steps to create A-matrix
Joint 1 is a ‘To’ joint for member 5
Thus we can fill in the 1st and 2nd row entries in the A-matrix for the F5 column
u1,5 =
(X4 – X1) i + (Y4 – Y1) j
u1,5 =
(L – L) i + (0 – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u1,5 =
(0) i + (-1) j
i.e. Row 1 - Joint 1 x-direction
Column 5 - force F5 column
Coefficient = 0
i.e. Row 2 - Joint 1 y-direction
Column 5 - force F5 column
Coefficient = 1

## Slide 16: Steps to create A-matrix
At joint 2:
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Connectivity
Members 1, 2, and 3 are connected at joint 2.
Note whether joint is a ‘From’ or ‘To’ joint for each member
Joint 2 is a ‘To’ joint for member 1
Joint 2 is a ‘From’ joint for member 2
Form the unit vector for each member force at the joint
Means we are dealing with the 3rd and 4th rows of the A-matrix
Get the members that are connected to joint 2.
Note the joint that connects to the other end of each member
Member 1 is connected from joint 1
Member 2 is connected to joint 3
Next, move to joint 2
Joint 2 is a ‘From’ joint for member 3
Member 3 is connected to joint 4

## Slide 17: Steps to create A-matrix
Form the unit vector for each member force at the joint
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
If join is a ‘From’ joint use:
Otherwise it is a ‘To’ joint, so use:
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Joint 2 is a ‘To’ joint for member 1
Thus we can fill in the 3rd and 4th row entries in the A-matrix for the F1 column
u2,1 =
(X1 – X2) i + (Y1 – Y2) j
u2,1 =
(L – 0) i + (L – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u2,1 =
(1) i + (0) j
i.e. Row 3 – Joint 2 x-direction
Column 1 - force F1 column
Coefficient = 1
i.e. Row 4 – Joint 2 y-direction
Column 1 - force F1 column
Coefficient = 0

## Slide 18: Steps to create A-matrix
Joint 2 is a ‘From’ joint for member 2
Thus we can fill in the 3rd and 4th row entries in the A-matrix for the F2 column
u2,2 =
(X3 – X2) i + (Y3 – Y2) j
u2,2 =
(0 – 0) i + (0 – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u2,2 =
(0) i + (-1) j
i.e. Row 3 – Joint 2 x-direction
Column 2 - force F2 column
Coefficient = 0
i.e. Row 4 – Joint 2 y-direction
Column 2 - force F2 column
Coefficient = -1

## Slide 19: Steps to create A-matrix
Joint 2 is a ‘From’ joint for member 3
Thus we can fill in the 3rd and 4th row entries in the A-matrix for the F3 column
u2,3 =
(X4 – X2) i + (Y4 – Y2) j
u2,3 =
(L – 0) i + (0 – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u2,3 =
(1/√2 ) i + (-1/√2) j
i.e. Row 3 – Joint 2 x-direction
Column 3 - force F3 column
Coefficient = 1/√2
i.e. Row 4 – Joint 2 y-direction
Column 3 - force F3 column
Coefficient = -1/√2

## Slide 20: Steps to create A-matrix
At joint 3:
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Connectivity
Members 2, and 4 are connected at joint 3.
Note whether joint is a ‘From’ or ‘To’ joint for each member
Joint 3 is a ‘To’ joint for member 2
Joint 3 is a ‘From’ joint for member 4
Form the unit vector for each member force at the joint
Means we are dealing with the 5th and 6th rows of the A-matrix
Get the members that are connected to joint 3.
Note the joint that connects to the other end of each member
Member 2 is connected from joint 2
Member 4 is connected to joint 4
Next, move to joint 3

## Slide 21: Steps to create A-matrix
Form the unit vector for each member force at the joint
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
If join is a ‘From’ joint use:
Otherwise it is a ‘To’ joint, so use:
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Joint 3 is a ‘To’ joint for member 2
Thus we can fill in the 5th and 6th row entries in the A-matrix for the F2 column
u3,2 =
(X2 – X3) i + (Y2 – Y3) j
u3,2 =
(0 – 0) i + (L – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u3,2 =
(0) i + (1) j
i.e. Row 5 – Joint 3 x-direction
Column 2 - force F2 column
Coefficient = 0
i.e. Row 6 – Joint 3 y-direction
Column 2 - force F2 column
Coefficient = 1

## Slide 22: Steps to create A-matrix
Joint 3 is a ‘From’ joint for member 4
Thus we can fill in the 5th and 6th row entries in the A-matrix for the F4 column
u3,4 =
(X4 – X3) i + (Y4 – Y3) j
u3,4 =
(L – 0) i + (0 – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u3,4 =
(1) i + (0) j
i.e. Row 5 – Joint 3 x-direction
Column 4 - force F4 column
Coefficient = 1
i.e. Row 6 – Joint 3 y-direction
Column 4 - force F4 column
Coefficient = 0

## Slide 23: Steps to create A-matrix
At joint 4:
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Connectivity
Members 3, 4, and 5 are connected at joint 4.
Note whether joint is a ‘From’ or ‘To’ joint for each member
Joint 4 is a ‘To’ joint for member 3
Joint 4 is a ‘To’ joint for member 4
Form the unit vector for each member force at the joint
Means we are dealing with the 7th and 8th rows of the A-matrix
Get the members that are connected to joint 4.
Note the joint that connects to the other end of each member
Member 3 is connected from joint 2
Member 4 is connected from joint 3
Next, move to joint 4
Joint 4 is a ‘From’ joint for member 5
Member 5 is connected to joint 1

## Slide 24: Steps to create A-matrix
Form the unit vector for each member force at the joint
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
If join is a ‘From’ joint use:
Otherwise it is a ‘To’ joint, so use:
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Joint 4 is a ‘To’ joint for member 3
Thus we can fill in the 7th and 8th row entries in the A-matrix for the F3 column
u4,3 =
(X2 – X4) i + (Y2 – Y4) j
u4,3 =
(0 – L) i + (L – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u4,3 =
(-1/√2) i + (1/√2) j
i.e. Row 7 – Joint 4 x-direction
Column 3 - force F3 column
Coefficient = -1/√2
i.e. Row 8 – Joint 4 y-direction
Column 3 - force F3 column
Coefficient = 1/√2

## Slide 25: Steps to create A-matrix
Joint 4 is a ‘To’ joint for member 4
Thus we can fill in the 7th and 8th row entries in the A-matrix for the F4 column
u4,4 =
(X3 – X4) i + (Y3 – Y4) j
u4,4 =
(0 – L) i + (0 – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u4,4 =
(-1) i + (0) j
i.e. Row 7 – Joint 4 x-direction
Column 4 - force F4 column
Coefficient = -1
i.e. Row 8 – Joint 4 y-direction
Column 4 - force F4 column
Coefficient = 0

## Slide 26: Steps to create A-matrix
Joint 4 is a ‘From’ joint for member 5
Thus we can fill in the 7th and 8th row entries in the A-matrix for the F5 column
u4,5 =
(X1 – X4) i + (Y1 – Y4) j
u4,5 =
(L – L) i + (L – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u4,5 =
(0) i + (1) j
i.e. Row 7 – Joint 4 x-direction
Column 5 - force F5 column
Coefficient = 0
i.e. Row 4 – Joint 2 y-direction
Column 5 - force F5 column
Coefficient = 1

## Slide 27: Steps to create A-matrix
Reaction 1 is at joint 3:
Means we are dealing with the 5th and 6th rows of the A-matrix
We are dealing with the R1 column, i.e. column 6
Next, enter coefficients for the reactions
Joint # | x-component direction | y-component direction
3 | 0 | 1
4 | 0 | 1
4 | 1 | 0
Reactions
We can fill in the 5th and 6th row entries in the A-matrix for the R1 column
i.e. Row 5 – Joint 3 x-direction
Column 6 – force R1 column
Coefficient = 0
i.e. Row 6 – Joint 3 y-direction
Column 6 – force R1 column
Coefficient = 1

## Slide 28: Steps to create A-matrix
Reaction 2 is at joint 4:
Means we are dealing with the 7th and 8th rows of the A-matrix
We are dealing with the R2 column, i.e. column 7
Joint # | x-component direction | y-component direction
3 | 0 | 1
4 | 0 | 1
4 | 1 | 0
Reactions
We can fill in the 7th and 8th row entries in the A-matrix for the R2 column
i.e. Row 7 – Joint 4 x-direction
Column 7 – force R1 column
Coefficient = 0
i.e. Row 8 – Joint 4 y-direction
Column 7 – force R1 column
Coefficient = 1

## Slide 29: Steps to create A-matrix
Reaction 3 is at joint 4:
Means we are dealing with the 7th and 8th rows of the A-matrix
We are dealing with the R3 column, i.e. column 8
Joint # | x-component direction | y-component direction
3 | 0 | 1
4 | 0 | 1
4 | 1 | 0
Reactions
We can fill in the 7th and 8th row entries in the A-matrix for the R2 column
i.e. Row 7 – Joint 4 x-direction
Column 8 – force R3 column
Coefficient = 1
i.e. Row 8 – Joint 4 y-direction
Column 8 – force R3 column
Coefficient = 0

## Slide 30: Steps to create b-matrix
External Force is at joint 1:
Means we are dealing with the 1st and 2nd rows of the b-matrix
Enter the know external forces
We can fill in the 1st and 2nd row entries in the b-matrix:
i.e. Row 1 – Joint 1 x-direction
Value = -1000
i.e. Row 2 – Joint 1 y-direction
Value = 0
External Forces
Joint # | x-component | y-component
1 | -FE = -1000 N | 0

## Slide 31: Truss Build GUI
Allows you to build up the truss and visualize it, and generate an input file to be used later with your own truss3d function
GUI builds a 3D truss, so cannot be loaded into the truss2d example. Both teams in each group build their own truss design and truss3d code.
GUI requires Matlab 2018a or greater and the Aerospace Toolbox
To test if you have the Aerospace Toolbox try:
  dcm2quat(eye(2))
Download the TrussAnalysis.mlapp and buildAmat.m and TrussReadInput.m also need to be downloaded in the same working directory. Make sure to save in a directory you have write access to, such as Z: drive or personal computer.